## Slide 1: MICROOPERATION
An elementary operation performed during
one clock pulse, on the information stored
in one or more registers
R  f(R, R)
f: shift, count, clear, load, add,...
ALU
(f)
Registers
(R)
1 clock cycle
Register Transfer Language

## Slide 2: REGISTER TRANSFER LANGUAGE
- Set of registers and their functions
- Microoperations Set
Set of allowable microoperations provided
by the organization of the computer
- Control signals that initiate the sequence of
microoperations
----> Register transfer language
- A symbolic language
- A convenient tool for describing the
internal organization of digital computers
- Can also be used to facilitate the design
process of digital systems.
Definition of the (internal) organization of a computer
For any function of the computer, a sequence of
microoperations is used to describe it
Register Transfer Language

## Slide 3: REGISTER TRANSFER
R1
Register
Numbering of bits
Showing individual bits
Subfields
PC(H)
PC(L)
15
8
7
0
- a register
- portion of a register
- a bit of a register
Common ways of drawing the block diagram of a register
A simultaneous transfer of all bits from the
source to the destination register, during one clock pulse
R2  R1
A binary condition(p=1) which determines when the transfer
is to occur
If (p=1) then (R2  R1)
P: R2  R1
7 6 5 4 3 2 1 0
R2
15
0
Designation of a register
Representation of a transfer(parallel)
Representation of a controlled(conditional) transfer
Register Transfer

## Slide 4: HARDWARE IMPLEMENTATION OF CONTROLLED TRANSFERS
Basic Symbols for Register Transfers
Implementation of controlled transfer
P: R2 R1
Block diagram
Timing diagram
Clock
Capital letters Denotes a register MAR, R2
and numerals
Parentheses ( ) Denotes a part of a register R2(0-7), R2(L)
Arrow  Denotes transfer of information R2  R1
Colon : Denotes termination of control function P:
Comma , Separates two micro-operations A  B, B  A
Symbols
Description Meaning
Register Transfer
Transfer occurs here
R2
R1
Control
Circuit
Load
P
n
Clock
Load
t
t+1

## Slide 5: Register Transfer
Data can move from register to register.
Digital logic used to process data
for example:
Register A
Register B
Register C
Digital Logic
Circuits
C  A + B

## Slide 6: Building a Computer
Needs:
processing
storage
communication
Notes: 6

## Slide 7
A1 | A0
B1 | B0
C1 | C0
D1 | D0
Mux 0
Mux 1
Bus 0
Bus 1
0
1
2
3
0
1
2
3
S1
S0

## Slide 9: Bus Transfer
For register R0 to R3 in a 4 bit system
S1
S0
4-line
common
bus
Register D
Register C
Register B
Register A
Used for highest bit from each register
Used for lowest bit

## Slide 10
The number of multiplexer needed to construct the bus=n n:number of bits in each register
The size of each multiplexer= k *1
  K: number of register
Example:
  Common bus for eight of register of 16-bit each, requires a 16 multiplexer of size 8X1 and 3 selection line

## Slide 11: Question
For register R0 to R63 in a 16 bit system:
  What is the MUX size we use?
  How many MUX we need?
  How many select bit?

## Slide 12: Three-State Bus Buffers
    A bus system can be constructed with three-state gates instead of multiplexers
    Tri-State : 0, 1, High-impedance(Open circuit)
    Buffer
      A device designed to be inserted between other devices to match impedance, to prevent mixed interactions.

## Slide 13: Tri-state buffer gate
    Tri-state buffer gate : Fig. 4-4
      When control input C=1 : The output is enabled(output Y = input A)
      When control input C=0 : The output is disabled(output Y = high-impedance)
Normal input A
Control input C
If C=1, Output Y = A
If C=0, Output = High-impedance

## Slide 14: The construction of a bus system with tri-state buffer
A0
B0
C0
D0
Select input
Enable input

## Slide 15: Memory Transfer
The transfer of information from a memory word to the outside environment is called a read operation
The transfer of new information to be stored into the memory is called a write operation

## Slide 16: Memory Read and Write
AR: address register
DR: data register
Read: DR  M[AR]
Write: M[AR]  R1
AR
Memory
unit
Read
Write
DR

## Slide 17
Summary of Register Transfer Microoperations
Bus and Memory Transfers
A   B Transfer content of reg. B into reg. A
AR  DR(AD) Transfer content of AD portion of reg. DR into reg. AR
A  constant Transfer a binary constant into reg. A
ABUS  R1, Transfer content of R1 into bus A and, at the same time,
R2  ABUS Transfer content of bus A into R2
M[R] Memory word specified by reg. R
M Equivalent to M[AR]
DR  M Memory read operation: transfers content of
memory word specified by AR into DR
M  DR Memory write operation: transfers content of
DR into memory word specified by AR

## Slide 18: ARITHMETIC MICROOPERATIONS
Four types of microoperations
- Register transfer microoperations
- Arithmetic microoperations
- Logic microoperations
- Shift microoperations
Arithmetic Microoperations

## Slide 19: Arithmetic Microoperations
Symbolic designation Description
R3 ← R1 + R2 Contents of R1 plus R2 transferred to R3 R3 ← R1 – R2 Contents of R1 minus R2 transferred to R3 R2 ← R2 Complement the contents of R2 (1’s complement) R2 ← R2 + 1 2’s Complement the contents of R2 (negate) R3 ← R1 + R2 + 1 R1 plus the 2’s complement of R2 (subtract) R1 ← R1 + 1 Increment the contents of R1 by one R1 ← R1 – 1 Decrement the contents of R1 by one
Multiplication and division are not basic arithmetic operations
  Multiplication : R0 = R1 * R2
  Division : R0 = R1 / R2

## Slide 20: Arithmetic Microoperations
A single circuit does both arithmetic addition and subtraction depending on control signals.
• Arithmetic addition:
R3  R1 + R2 (Here + is not logical OR. It denotes addition)

## Slide 21: Arithmetic Microoperations
Arithmetic subtraction:
R3 R1 + R2 + 1
where R2 is the 1’s complement of R2.
Adding 1 to the one’s complement is equivalent to taking the 2’s complement of R2 and adding it to R1.

## Slide 22: BINARY ADDER
Binary adder is constructed with full-adder circuits connected in cascade.

## Slide 23: BINARY ADDER-SUBTRACTOR
• The addition and subtraction operations cane be combined into one common circuit by including an exclusive-OR gate with each full-adder.
XOR
M b
0 0 0
0 1 1
1 0 1
1 1 0

## Slide 24: BINARY ADDER-SUBTRACTOR
M = 0: Note that B XOR 0 = B. This is exactly the same as the binary adder with carry in C0 = 0.
  M = 1: Note that B XOR 1 = B (flip all B bits). The outputs of the XOR gates are thus the 1’s complement of B.
  M = 1 also provides a carry in 1. The entire operation is: A + B + 1.
For unsigned number this give A-B if A>=B or the 2’s complement of (B-A) if A<B

## Slide 25: BINARY ADDER-SUBTRACTOR

## Slide 26: 4-bit Binary Incrementer
    Adds one to a number in a register
    Sequential circuit implementation using binary counter
    Combinational circuit implementation using Half Adder
    The least significant HA bit is connected to logic-1
    The output carry from one HA is connected to the input of the next-higher-order HA

## Slide 27: 4-bit Binary Incrementer
B3 B2 B1 B0 1
Always added to 1
C4
S3 S2 S1 S0

## Slide 28: BINARY ADDER
Binary Adder-Subtractor
Binary Incrementer
Binary Adder
Arithmetic Microoperations

## Slide 29
D=A+Y+Cn

## Slide 30: ARITHMETIC CIRCUIT
S1
S0
0
1
2
3
4x1
MUX
X0
Y0
C0
C1
D0
FA
S1
S0
0
1
2
3
4x1
MUX
X1
Y1
C1
C2
D1
FA
S1
S0
0
1
2
3
4x1
MUX
X2
Y2
C2
C3
D2
FA
S1
S0
0
1
2
3
4x1
MUX
X3
Y3
C3
C4
D3
FA
Cout
A0
B0
A1
B1
A2
B2
A3
B3
0
1
S0
S1
Cin
S1 S0 Cin Y Output Microoperation
0 0 0 B D = A + B Add
0 0 1 B D = A + B + 1 Add with carry
0 1 0 B’ D = A + B’ Subtract with borrow
0 1 1 B’ D = A + B’+ 1 Subtract
1 0 0 0 D = A Transfer A
1 0 1 0 D = A + 1 Increment A
1 1 0 1 D = A - 1 Decrement A
1 1 1 1 D = A Transfer A
Arithmetic Microoperations

## Slide 32: LOGIC MICROOPERATIONS
Specify binary operations on the strings of bits in registers.
- useful for bit manipulations on binary data
AND: Mask out certain group of bits
OR : Merge binary or character data
- useful for making logical decisions based on the bit value
Use ۷ to denote OR and ۸ to denote AND
Use + only with production not with registers.
P+Q: R1R2+R3 , R4  R5 ۷ R6
Logic Microoperations

## Slide 35: 4.5 Logic Microoperations
  Manipulating the bits stored in a register
Logic Microoperations
Notes: 35

## Slide 37
• A variety of logic gates are inserted for each bit of registers. Different bitwise logical operations are selected by select signals.
LOGIC CIRCUIT
Notes: 37

## Slide 38: Example
Extend the previous logic circuit to accommodate XNOR, NAND, NOR, and the complement of the second input.
S2 | S1 | S0 | Output | Operation
0 | 0 | 0 | X  Y | AND
0 | 0 | 1 | X  Y | OR
0 | 1 | 0 | X Å Y | XOR
0 | 1 | 1 | A | Complement A
1 | 0 | 0 | (X  Y) | NAND
1 | 0 | 1 | (X  Y) | NOR
1 | 1 | 0 | (X Å Y) | XNOR
1 | 1 | 1 | B | Complement B
Notes: 38

## Slide 39: More Logic Microoperation
TABLE 4-6. Sixteen Logic Microoperations
X Y F0 F1 F2 F3 F4 F5 F6 F7 F8 F9 F10 F11 F12 F13 F14 F15
0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1 0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1 1 0 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
TABLE 4-5. Truth Table for 16 Functions of Two Variables
Boolean function Microoperation Name
F0 = 0 F ← 0 Clear F1 = xy F ← A∧B AND F2 = xy’ F ← A∧B F3 = x F ← A Transfer A F4 = x’y F ← A∧B F5 = y F ← B Transfer B F6 = x  y F ← A B Ex-OR F7 = x+y F ← A∨B OR
Boolean function Microoperation Name
F8 = (x+y)’ F ← A∨B NOR F9 = (x  y)’ F ← A B Ex-NOR F10 = y’ F ← B Compl-B F11 = x+y’ F ← A∨B F12 = x’ F ← A Compl-A F13 = x’+y F ← A∨B F14 = (xy)’ F ← A∧B NAND F15 = 1 F ← all 1’s set to all 1’s
Notes: 39

## Slide 40: Homework 1
Design a multiplexer to select one of the 16 previous functions.
Notes: 40

## Slide 41: Selective-set

## Slide 42: Selective-complement

## Slide 43: Selective-clear

## Slide 44: Mask

## Slide 45: Insert

## Slide 46: Clear_Example
  Logic operation can…
    clear a group of bit values (Anding the bits to be cleared with zeros)
    10101101 10101011 R1 (data)
    00000000 11111111 R2 (mask)
    00000000 10101011 R1

## Slide 47: Set_Example
  set a group of bit values (Oring the bits to be set to ones with ones)
  10101101 10101011 R1 (data)
  11111111 00000000 R2 (mask)
  11111111 10101011 R1

## Slide 48: Insert_Example
    Insert
      The insert operation inserts a new value into a group of bits
      This is done by first masking the bits and then ORing them with the required value
1) Mask 2) OR
0110 1010 A before 0000 1010 A before
0000 1111 B mask 1001 0000 B insert
0000 1010 A after mask A  B 1001 1010 A after insert AVB

## Slide 49: Complement_Example
  Complement a group of bit values (Exclusively Or (XOR) the bits to be complemented with ones)
  10101101 10101011 R1 (data)
  11111111 00000000 R2 (mask)
  01010010 10101011 R1

## Slide 50: 4-6 Shift Microoperations
Shift example: 11000
Shift Microoperations :
    Shift microoperations are used for serial transfer of data
    Three types of shift microoperation : Logical, Circular, and Arithmetic

## Slide 51: Shift Microoperations
Symbolic designation Description
R ← shl R Shift-left register R R ← shr R Shift-right register R R ← cil R Circular shift-left register R R ← cir R Circular shift-right register R R ← ashl R Arithmetic shift-left R R ← ashr R Arithmetic shift-right R
TABLE 4-7. Shift Microoperations

## Slide 52: Logical Shift
    A logical shift transfers 0 through the serial input
    The bit transferred to the end position through the serial input is assumed to be 0 during a logical shift (Zero inserted)
0
0

## Slide 53: Logical Shift Example
1. Logical shift: Transfers 0 through the serial input.
R1 ¬ shl R1 Logical shift-left
R2 ¬ shr R2 Logical shift-right
(Example) Logical shift-left
10100011  01000110

## Slide 54: Circular Shift
    The circular shift circulates the bits of the register around the two ends without loss of information

## Slide 55: Circular Shift Example
Circular shift-left
Circular shift-right
(Example) Circular shift-left
10100011 is shifted to 01000111

## Slide 56: Arithmetic Shift
    An arithmetic shift shifts a signed binary number to the left or right
    An arithmetic shift-left multiplies a signed binary number by 2
    An arithmetic shift-right divides the number by 2
    In arithmetic shifts the sign bit receives a special treatment

## Slide 57: Arithmetic Shift Right
Arithmetic right-shift: Rn-1 remains unchanged;
Rn-2 receives Rn-1, Rn-3 receives Rn-2, so on.
For a negative number, 1 is shifted from the sign bit to the right. A negative number is represented by the 2’s complement. The sign bit remained unchanged.

## Slide 58: Arithmetic Shift Right
Arithmetic Shift Right :
  Example 1
0100 (4) 
0010 (2)
  Example 2
1010 (-6) 
1101 (-3)

## Slide 59: Arithmetic Shift Left
LSB
Carry out
Sign bit
Rn-1
Rn-2
Vs=1 : Overflow Vs=0 : use sign bit
LSB
0 insert
The operation is same with Logic shift-left
The only difference is you need to check overflow problem

## Slide 60: Arithmetic Shift Left
Arithmetic Shift Left :
  Example 1
0010 (2) 
0100 (4)
  Example 2
1110 (-2) 
1100 (-4)

## Slide 61: Arithmetic Shift Left
Arithmetic Shift Left :
  Example 3
0100 (4) 
1000 (overflow)
  Example 4
1010 (-6) 
0100 (overflow)